## Slide 1: IMSE 991 Multiple Criteria Decision Making
Lecture 9
PROMETHEE

## Slide 2: Mid Term Exam Review
Exam Review

## Slide 3: PROMETHEE
Outranking Methods
PROMETHEE I
PROMETHEE II

## Slide 4: Outranking Methods
The underlying idea for the development of the outranking methods is to reveal a relation in between the dominance relation and the multi attribute value function
Outranking methods are used to enrich the dominance relation by some elements
Most outranking methods are non-compensatory

## Slide 5: Outranking Methods
Example of Outranking Relationship
  DM considers three cars based on two attributes
    A1 = ($13,000, 18 MPG)
    A2 = ($16,000, 21 MPG)
    A3 = ($18,000, 25 MPG)
  Alternatives non-dominate each other
  No preference yet
  But…a prior “likely preferred to” relationship may exist in the DM’s mind

## Slide 6: Outranking Methods
Example of Outranking Relationship
  The DM may prefer A1 to A2 because he or she does not want to pay an extra $3,000 for the 3 MPG improvement
  Therefore, it defines that A1 outranks A2
  Other preferences between alternatives also exist, but the preferences do not have to be transitive

## Slide 7: Outranking Methods
Expression of Outranking Relationship
  Expressed using the binary relationship R
  Notation (Ap R Aq) or (Ap → Aq)
    Means Ap outranks Aq
  Although two alternatives Ap and Aq do not dominate each other, it is realistic to accept the risk of regarding Ap as better Aq
  Again, the outranking relationship R is not required to be transitive

## Slide 8: Outranking Methods
Incomparability
  When a DM must compare two alternatives, they will react in one of the three following ways:
    Preference for one of them
    Indifference between them
    Refusal or inability to compare them

## Slide 9: Outranking Methods
Incomparability
  Two alternatives can perfectly remain incomparable without endangering the decision aid procedure
  A conclusion of incomparability between some alternatives may also be quite helpful since it puts forward some aspects of the problem which would perhaps deserve a more thorough study

## Slide 10: PROMETHEE
The acronym PROMETHEE stands for ‘Preference Ranking Organization METHod for Enriched Evaluation.’
Provides the decision maker with ranking actions (choices or alternatives) based on preference degrees

## Slide 11: PROMETHEE
There are three main steps in the computational process
  Computation of preference degrees for every ordered pair of actions on each criterion
  Computation of unicriterion flows
  Computation of global flows
Based on the global flows, a ranking of the actions will be obtained as well as a graphical representation of the decision problem

## Slide 12: PROMETHEE
Case Study 6.1
  Buying a new car
    Price (minimized)
    Consumption (minimized)
    Comfort (maximized)
    Power (maximized)

## Slide 13: PROMETHEE
Case Study Data
Raw Data | Price | Consumption (km/l) | Comfort | Power (cc)
Min/Max | MIN | MIN | MAX | MAX
Economic | 15000 | 7.5 | Very Bad | 50
Sport | 29000 | 9 | Bad | 110
Luxury | 38000 | 8.5 | Very Good | 90
Touring A | 24000 | 8 | Average | 75
Touring B | 25500 | 7 | Average | 85
Numeric Comfort
MAX
1
4
10
8
8
Conversion of qualitative value to numeric representation

## Slide 14: PROMETHEE
Unicriterion Preference Degrees
  Preference degree – a score between 0 and 1 which expresses how an action is preferred over another action by the decision maker
    Preference degree of 1 means a total or strong preference
    Preference degree of 0 means there is no preference at all
    Preference between 0 and 1 is somewhere in between the two

## Slide 15: PROMETHEE
Unicriterion Preference Degrees
  Pairwise preference degree of action A over action B, but the reverse is not true
  Unicriterion preference degree is computed through rescaling or enriching the evaluations of the actions by means of preference information
  It is important how the decision maker perceives the difference on every specific criterion

## Slide 16: PROMETHEE
Preference functions
  Two general types of preference functions discussed
    Linear – gradual increase
      Two parameters are necessary
        q = indifference threshold
        p = preference threshold
    Gaussian – exponential function
      One parameter is necessary
        s = inflection point
    Describe the preference relationships

## Slide 17: PROMETHEE
1
0
q p
Linear preference function
1
0
s
Gaussian preference function
Preference functions

## Slide 18: PROMETHEE
Three linear preference functions
1
0
q = p = 0
A strong preference for action as soon as there is a difference
1
0
q = 0 p
No Indifference zone
1
0.5
0
q p
Step function that can only take 3 values

## Slide 19: PROMETHEE
Definition of evaluation terms
  The set of actions to be ranked
    A = {a1, a2, …, an)
  The set of criteria
    F = {f1, f2, …, fm)
  The evaluation of action aj on criterion fi = fi(aj)
  The difference between evaluations
    d = fk(a1) - fk(aj)

## Slide 20: PROMETHEE
Criterion with Linear Preference
  Pk(ai,aj) =
Level Criterion
  Pk(ai,aj) =
Pk(ai,aj)
pk
Criterion III
1
d
Criterion IV
qk
pk
0.5
1
Pk(ai,aj)
d

## Slide 21: PROMETHEE
Criterion With Indifference Area.
  Pk(ai,aj) =
Gaussian Criterion
  Pk(ai,aj) =
qk
pk
Criterion V
1
Pk(ai,aj)
d
sk
Criterion VI
1
Pk(ai,aj)
d

## Slide 22
Case Study 6.1
  Preference Parameters of all the criteria
Criterion | Function | wi | qi | pi
price | linear | 0.25 | 2000 | 5000
consumption | linear | 0.25 | 0.5 | 1
comfort | linear | 0.25 | 1 | 2
power | linear | 0.25 | 10 | 20

## Slide 23: PROMETHEE
Unicriterion preference degrees for price with a linear function when p = 5000 and q = 2000
  Diagonals are 0 because an action cannot be preferred to itself
  Economic is the cheapest and base point for comparison
  Difference between Economic and Sport is 14000 so it is greater than the preference threshold p = 5000 and 0
  Touring A and Touring B difference is 1500 so no preference between the cars
  Touring B is cheaper than Sport so perform the following computation

## Slide 24: PROMETHEE
Computation of the preference degree between the Touring B and Sport autos
  Difference is 3500 and q = 2000 and p = 5000
2000 3500 5000
1
0.5
0
(3500 – 2000)/(5000-2000) = 0.5

## Slide 25: PROMETHEE
Price (minimized):
  Unicriterion preference degrees with a linear function when q = 2000 and p = 5000 and
Difference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | -14000 | -23000 | -9000 | -10500
Sport | 14000 | 0 | -9000 | 5000 | 3500
Luxury | 23000 | 9000 | 0 | 14000 | 12500
Touring A | 9000 | -5000 | -14000 | 0 | -1500
Touring B | 10500 | -3500 | -12500 | 1500 | 0
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 1 | 1 | 1 | 1
Sport | 0 | 0 | 1 | 0 | 0
Luxury | 0 | 0 | 0 | 0 | 0
Touring A | 0 | 1 | 1 | 0 | 0
Touring B | 0 | 0.5 | 1 | 0 | 0
Raw Data | Price | Consumption (km/l) | Comfort | Power (cc)
Min/Max | MIN | MIN | MAX | MAX
Economic | 15000 | 7.5 | Very Bad | 50
Sport | 29000 | 9 | Bad | 110
Luxury | 38000 | 8.5 | Very Good | 90
Touring A | 24000 | 8 | Average | 75
Touring B | 25500 | 7 | Average | 85

## Slide 26: PROMETHEE
Graphical Representation of the Preferences
  If the preference of car A over car B is greater than 0, then there is an arrow from A to B
  Strength is represented by the arrow
Economic
Touring A
Touring B
Sport
Luxury
`

## Slide 27: PROMETHEE
Consumption (minimized):
  Unicriterion preference degrees with a linear function when q = 0.5 and p = 1.0
Difference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | -1.5 | -1 | -0.5 | 0.5
Sport | 1.5 | 0 | 0.5 | 1 | 2
Luxury | 1 | -0.5 | 0 | 0.5 | 1.5
Touring A | 0.5 | -1 | -0.5 | 0 | 1
Touring B | -0.5 | -2 | -1.5 | -1 | 0
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 1 | 1 | 0 | 0
Sport | 0 | 0 | 0 | 0 | 0
Luxury | 0 | 0 | 0 | 0 | 0
Touring A | 0 | 1 | 0 | 0 | 0
Touring B | 0 | 1 | 1 | 1 | 0

## Slide 28: PROMETHEE
Comfort (maximized):
  Unicriterion preference degrees with a linear function when q = 1 and p = 2
Difference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | -3 | -9 | -7 | -7
Sport | 3 | 0 | -6 | -4 | -4
Luxury | 9 | 6 | 0 | 2 | 2
Touring A | 7 | 4 | -2 | 0 | 0
Touring B | 7 | 4 | -2 | 0 | 0
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0 | 0 | 0 | 0
Sport | 1 | 0 | 0 | 0 | 0
Luxury | 1 | 1 | 0 | 1 | 1
Touring A | 1 | 1 | 0 | 0 | 0
Touring B | 1 | 1 | 0 | 0 | 0

## Slide 29: PROMETHEE
Power (maximized):
  Unicriterion preference degrees with a linear function when q = 10 and p = 20
Difference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | -60 | -40 | -25 | -35
Sport | 60 | 0 | 20 | 35 | 25
Luxury | 40 | -20 | 0 | 15 | 5
Touring A | 25 | -35 | -15 | 0 | -10
Touring B | 35 | -25 | -5 | 10 | 0
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0 | 0 | 0 | 0
Sport | 1 | 0 | 1 | 1 | 1
Luxury | 1 | 0 | 0 | 0.5 | 0
Touring A | 1 | 0 | 0 | 0 | 0
Touring B | 1 | 0 | 0 | 0 | 0

## Slide 30: PROMETHEE
Unicriterion positive, negative and net flows
  Difficult to draw conclusions from the preference degree tables
  Summarized into
    Leaving or positive flows
    Entering or negative flows
    Net flows
  Measure how an action is preferred over all other actions

## Slide 31: Necessary Calculations
Multiattribute Preference Index
  p(ai,aj) =
Weight each of the matrices with the criteria weights
Criterion | wi
Price | 0.25
Consumption | 0.25
Comfort | 0.25
Power | 0.25

## Slide 32: Necessary Calculations
Weight each of the matrices
Weighted Pairwise Comparison Matrix for Price |  |  |  |  | 
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0.25 | 0.25 | 0.25 | 0.25
Sport | 0 | 0 | 0.25 | 0 | 0
Luxury | 0 | 0 | 0 | 0 | 0
Touring A | 0 | 0.25 | 0.25 | 0 | 0
Touring B | 0 | 0.125 | 0.25 | 0 | 0
Weighted Pairwise Comparison Matrix for Consumption |  |  |  |  | 
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0.25 | 0.25 | 0 | 0
Sport | 0 | 0 | 0 | 0 | 0
Luxury | 0 | 0 | 0 | 0 | 0
Touring A | 0 | 0.25 | 0 | 0 | 0
Touring B | 0 | 0.25 | 0.25 | 0.25 | 0

## Slide 33: Necessary Calculations
Weight each of the matrices
Weighted Pairwise Comparison Matrix for Comfort |  |  |  |  | 
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0 | 0 | 0 | 0
Sport | 0.25 | 0 | 0 | 0 | 0
Luxury | 0.25 | 0.25 | 0 | 0.25 | 0.25
Touring A | 0.25 | 0.25 | 0 | 0 | 0
Touring B | 0.25 | 0.25 | 0 | 0 | 0
Weighted Pairwise Comparison Matrix for Power |  |  |  |  | 
Pref. Price | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0 | 0 | 0 | 0
Sport | 0.25 | 0 | 0.25 | 0.25 | 0.25
Luxury | 0.25 | 0 | 0 | 0.125 | 0
Touring A | 0.25 | 0 | 0 | 0 | 0
Touring B | 0.25 | 0 | 0 | 0 | 0

## Slide 34: Necessary Calculations
Weighted Pairwise Matrix – Across all criteria
Sum of the weighted pairwise comparison matrix across all criterion
Computation of the weighted pairwise preference matrix |  |  |  |  | 
Preference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0.5 | 0.5 | 0.25 | 0.25
Sport | 0.5 | 0 | 0.5 | 0.25 | 0.25
Luxury | 0.5 | 0.25 | 0 | 0.375 | 0.25
Touring A | 0.5 | 0.75 | 0.25 | 0 | 0
Touring B | 0.5 | 0.625 | 0.5 | 0.25 | 0

## Slide 35: Necessary Calculations
Leaving Flow
Entering Flow
Net Flow

## Slide 36: PROMETHEE
Positive flows
  Indicates how an action is preferred over all other actions
  Sum across each action and divide by (n-1)
Preference | Economic | Sport | Luxury | Touring A | Touring B | Φ+(a)
Economic | 0 | 0.5 | 0.5 | 0.25 | 0.25 | 0.375
Sport | 0.5 | 0 | 0.5 | 0.25 | 0.25 | 0.375
Luxury | 0.5 | 0.25 | 0 | 0.375 | 0.25 | 0.34375
Touring A | 0.5 | 0.75 | 0.25 | 0 | 0 | 0.375
Touring B | 0.5 | 0.625 | 0.5 | 0.25 | 0 | 0.46875

## Slide 37: PROMETHEE
Negative net flow
  Sum between each action and divide by (n-1)
Preference | Economic | Sport | Luxury | Touring A | Touring B
Economic | 0 | 0.5 | 0.5 | 0.25 | 0.25
Sport | 0.5 | 0 | 0.5 | 0.25 | 0.25
Luxury | 0.5 | 0.25 | 0 | 0.375 | 0.25
Touring A | 0.5 | 0.75 | 0.25 | 0 | 0
Touring B | 0.5 | 0.625 | 0.5 | 0.25 | 0
Φ-(a) | 0.5 | 0.53125 | 0.4375 | 0.28125 | 0.1875

## Slide 38: PROMETHEE
Positive and Negative Net Flows
Net Flows |  | 
 | Positive Net Flows | Negative Net Flows
Economic | 0.375 | 0.5
Sport | 0.375 | 0.53125
Luxury | 0.34375 | 0.4375
Touring A | 0.375 | 0.28125
Touring B | 0.46875 | 0.1875

## Slide 39: PROMETHEE
Positive Outranking Flow
  The positive outranking flow expresses how an alterative a is outranking all of the others
  It is its power, its outranking character
  The higher Φ+(a), the better the alternative

## Slide 40: PROMETHEE
Negative Outranking Flow
  The negative outranking flow expresses how an alterative a is outranked by all the others.
  It is its weakness, its outranked character.
  The lower Φ-(a), the better the alternative

## Slide 41: PROMETHEE I
PROMETHEE I ranking is based on the positive and negative net flows
Two complete preorders are built:
  Ranking the alternatives following the decreasing order of leaving flows
  Ranking the alternatives following the increasing order of entering flows
The intersection of the preorders yields the partial preorder

## Slide 42: PROMETHEE I
Partial Ranking

## Slide 43: PROMETHEE II
A unique complete preorder is built:
  Ranking the alternatives following the decreasing order of net flows

## Slide 44: PROMETHEE II
Overall net flows
  Subtract the negative flows from the positive flows
  Net score lies between -1 and 1
Net Flows |  |  | 
 | Positive Net Flows | Negative Net Flows | Total Net Flows
Economic | 0.375 | 0.5 | -0.125
Sport | 0.375 | 0.53125 | -0.15625
Luxury | 0.34375 | 0.4375 | -0.09375
Touring A | 0.375 | 0.28125 | 0.09375
Touring B | 0.46875 | 0.1875 | 0.28125

## Slide 45: PROMETHEE II
Total Net Flows
Chart: 
| Economic | Sport | Luxury | Touring A | Touring B
Total Net Flows | -0.125 | -0.15625 | -0.09375 | 0.09375 | 0.28125

## Slide 46: Properties of the Net Flow
Unicriterion net flows:

## Slide 47: Unicriterion Net Flows
Unicriterion Net Flows
Unicriterion Net Flows |  |  |  | 
 | Price Net Flows | Consumption Net Flows | Comfort Net Flows | Power Net Flows
Economic | 1 | 0.5 | -1 | -1
Sport | -0.375 | -0.75 | -0.5 | 1
Luxury | -1 | -0.5 | 1 | 0.125
Touring A | 0.25 | 0 | 0.25 | -0.125
Touring B | 0.125 | 0.75 | 0.25 | 0

## Slide 48: Weighted Unicriterion Net Flows
Weighted Unicriterion Net Flows
Weighted Unicriterion Net Flows |  |  |  | 
 | Price Net Flows | Consumption Net Flows | Comfort Net Flows | Power Net Flows
Economic | 0.25 | 0.125 | -0.25 | -0.25
Sport | -0.09375 | -0.1875 | -0.125 | 0.25
Luxury | -0.25 | -0.125 | 0.25 | 0.03125
Touring A | 0.0625 | 0 | 0.0625 | -0.03125
Touring B | 0.03125 | 0.1875 | 0.0625 | 0

## Slide 49: Weighted Unicriterion Net Flows
Weighted Unicriterion Net Flow Dieagram
Chart: Weighted Unicriterion Net Flows
| Economic | Sport | Luxury | Touring A | Touring B
Price Net Flows | 0.25 | -0.09375 | -0.25 | 0.0625 | 0.03125
Consumption Net Flows | 0.125 | -0.1875 | -0.125 | 0 | 0.1875
Comfort Net Flows | -0.25 | -0.125 | 0.25 | 0.0625 | 0.0625
Power Net Flows | -0.25 | 0.25 | 0.03125 | -0.03125 | 0

## Slide 50: PROMETHEE II
Complete Ranking
 | Rank | Total NF |  |  | Rank | Total NF |  |  | Rank | Total NF |  |  | Rank | Total NF |  |  | Rank | Total NF
Touring B | 1 | 0.281 |  | Touring A | 2 | 0.094 |  | Luxury | 3 | -0.094 |  | Economic | 4 | -0.125 |  | Sport | 5 | -0.156

## Slide 51: GAIA
Visual representation of a decision problem
Uses the Unicriterion Net flows computed by the PROMETHEE method
M (n x k) matrix – Single Criterion Net Flows

## Slide 52: GAIA
N alternatives can be represented as a cloud of n points in a k-dimensional space
The cloud is centered at the origin
With the number of criteria larger than 2, it is impossible to obtain a clear view of the relative positions of the points with regard to the criteria
We project the information in the k-dimensional space on a plane.
We project both the points and the unit vectors of the coordinate-axes representing the criteria

## Slide 53: GAIA
Projection on the GAIA plane

## Slide 54: GAIA
The GAIA plane is the plane for which as much information as possible is preserved after projection
The GAIA plane is as meta model (model of a model)

## Slide 55: GAIA
Alternatives and criteria in the GAIA plane

## Slide 56: GAIA
Properties associated with GAIA
  P1: The longer a criterion axis on the GAIA plane, the more discriminating this criterion
  P2: Criteria expressing similar preferences are represented by axes oriented in approximately the same direction
  P3: Criteria expressing conflicting preferences are oriented in opposite directions

## Slide 57: GAIA
Properties associated with GAIA
  P4: Criteria that are not related to each other in terms of preferences are represented by orthogonal axes.
  P5: Similar alternatives are represented by points located close to each other
  P6: Alternatives being good on a particular criterion are represented by points located in the direction of the corresponding criterion axis.

## Slide 58: GAIA
Interpretation
  Criteria g1 and g3 are expressing similar preferences and that the alternatives a1 and a5 are rather good on these criteria.
  Criteria g6 and g4 are also expressing similar preferences and that the alternatives a2, a7, a8 are rather good on them
  Criteria g2 and g5 are rather independent

## Slide 59: GAIA
Interpretation
  Criteria g1 and g3 are strongly conflicting with criteria g4 and g2
  Alternatives a1, a5 and a6 are rather good on the criteria g1, g3 and g5
  Alternatives a2, a7 and a8 are rather good on the criteria g6, g4 and g2
  Alternatives a3 and a4 are never good, never bad on all the criteria

## Slide 60: IMSE 991 Multiple Criteria Decision Making
Lecture 9
PROMETHEE