## Slide 1: IMSE 991 Multiple Criteria Decision Making
Lecture 12
Investment Strategy for Product Development in the Aerospace Industry

## Slide 2: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  This study shows the process used for the development of an investment strategy for the Air Force Material command that develops products for the military aerospace industry.
  There is a diverse set of projects, and it requires a set of goals, objectives, and metrics that can equally represent the projects so they can be compared with each other.

## Slide 3: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  We then determine the best list of projects to fund with the budget constraints.
  This approach is used to facilitate the Air Force in establishing their goals and objectives and relating them to decision criteria that can be used to analytically prioritize programs and allocate resources for the military projects.

## Slide 4: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  This approach requires the Executive Group, a group of senior managers in the Air Force Material command, to critically examine their goals and objectives and their relative importance in the final decision.
  The decision criteria and measures are then developed to provide a means to evaluate Decision Packages (DPs), which are proposed research and development projects for the military.

## Slide 5: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  The DPs are then ranked using these decision criteria and measures and their relative importance to allocate resources based on the goals and objectives.
  The challenge to ranking the DPs lies in the wide range of activities covered and to determine a set of criteria that is applicable across the wide range of activities.

## Slide 6: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  Group decision-making techniques are used to provide a means for developing the goals, objectives, and decision criteria used in the decision process and weighting the importance of the objectives and criteria.
  All the decision makers had input in the final decision process ensuring objectivity in the DP evaluation process.

## Slide 7: Investment Strategy for Product Development in the Aerospace Industry
Introduction
  The various viewpoints of the members of the Executive Group and others are captured and a group consensus/tolerance is achieved in a set of decision criteria.
  The investment strategy developed in this process provides the foundation for establishing an objective, automated structured project prioritization and resource allocation process with a traceable and defensible basis for investment decisions.

## Slide 8: Investment Strategy for Product Development
Establish Goals and Objectives and Decision Criteria
  The general approach used to establish the goals and decision criteria is shown in the following slide.
  Various techniques, such as surveys, group discussions, working group meetings, individual review and feedback consolidation, were used to arrive at the resulting list of the military’s goals, decision criteria, measures, and resource allocation constraints.

## Slide 9: Investment Strategy for Product Development

## Slide 10: Investment Strategy for Product Development
Establish Goals and Objectives and Decision Criteria
  The first step develops the initial framework for the goals, objectives, and decision criteria that are used for the DP evaluation process.
  Key decision makers must be identified, a reasonable set of initial of goals, objectives, and decisions must be established to provide a starting point for the executives.
  Key budgetary considerations must also be identified so the framework for the process can be discussed and agreed upon by the group.

## Slide 11: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Establish "straw man" list of goals and decision criteria
      A working group of facilitators developed a "straw man" list of goals and decision criteria.
      Provided the Executive Group with a starting point in establishing the military’s technical goals and decision criteria that are used to evaluate decision packages.

## Slide 12: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Conduct Executive Group surveys
      The process used to develop the military’s goals and objectives with the Executive Group is a version of the Nominal Group Technique (NGT).
      Surveys with the Executive Group are then conducted to establish key goals and decision criteria to be used to evaluate decision packages beyond core programs.
      The "straw man" list developed initially was used as a starting point for the surveys; however, it changes significantly early in the survey process.

## Slide 13: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Conduct Executive Group surveys
      Each Executive Group member is asked to brainstorm their ideas for goals and decision criteria.
      Suggestions from each of the members of the Executive Group are discussed and used to prompt the other members.
      The survey results are documented and provided to the Executive Group for their feedback.

## Slide 14: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Executive Group and working group meetings and manager’s feedback
      The goals and decision criteria developed in the survey process are documented and then presented to the Executive Group.
      A working group is assigned to refine and consolidate the goal and decision criteria and develop specific measures associated with the decision criteria.

## Slide 15: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Executive Group and working group meetings and manager’s feedback
      The results from the working group are documented and provided to the Executive Group for review.
      Changes to the criteria set are documented based on feedback from the Executive Group and are sent to the managers working for the Executive Group for their review and feedback.
      Their changes are incorporated into the goal and decision criteria data set.

## Slide 16: Investment Strategy for Product Development
Goals, Objectives, and Decision Criteria
  Key Steps
    Finalized list of goals and decision criteria
      The results in the finalized list of goals and decision criteria for evaluating DPs.

## Slide 17: Investment Strategy for Product Development
Technical Goals
  Goal 1—Satisfy customer needs.
  Goal 2—Make a difference for the military in this technical area.
  Goal 3—Have a transition strategy/technology plan.
For each goal, a set of decision criteria is developed to provide measures to evaluate the achievement of those goals.
Each high level goals has associated decision criteria

## Slide 18: Investment Strategy for Product Development
Goal 1—Satisfy customer needs.
  1.a Documentable customer need
  1.b Broad applicability
  1.c Importance of need to the military
  1.d Breakthrough

## Slide 19: Investment Strategy for Product Development
Goal 2—Make a difference for the military in this technical area.
  2.a Leadership
  2.b Adequate funding
  2.c Adequate work years
  2.c Payoff
  2.d Soundness of technical approach

## Slide 20: Investment Strategy for Product Development
Goal 3—Have a transition strategy/technology plan.
  3.a Customer flow
  3.b Risk of transition strategy/technology plan
  3.c Leverage of other resources

## Slide 21: Investment Strategy for Product Development
Budgeting Constraints
  Total Budget - Total funds available to the Materials Directorate.
  DP Budget - Total funds available to the Materials Directorate for applied research and development activities.

## Slide 22: Investment Strategy for Product Development
Budgeting Constraints
  Development Cycle Percentage Allocation of Resources - The percentage of available funds to be allocated to research and development activities based on the time required to complete the activities.
    Near Term (25%)
    Mid Term (50%)
    Far Term (25%)

## Slide 23: Investment Strategy for Product Development
Budgeting Constraints
  Directed/Fenced Dollars - The funds that are designated for a specific project or use.
  Space-Related Project - Whether this project is a space related project.

## Slide 24: Investment Strategy for Product Development
Budgeting Constraints
  Strategic Emphasis Areas - The percentage of available funds to be allocated to meet fundamental technology development requirements.
    Structures
    Propulsion
    Electronics, Optics, Survivability
    Non-structural
  Minimum Number of DPs Funded - The minimum number of DPs to be funded per Direction (focus area). All Directions must have at least one DP funded before any can have more than 1.

## Slide 25: Investment Strategy for Product Development
Develop Decision Criteria Definitions and Measures
  Development parameters
    Goals and decision criteria must represent actual and important considerations in making DP funding decisions.
    Decision criteria must differentiate one project from another in terms of higher or lower priority.

## Slide 26: Investment Strategy for Product Development
Develop Decision Criteria Definitions and Measures
  Development parameters
    Decision criteria must be independent, not overlapping in content or intent, to avoid accounting for the same thought or idea more than once.
    Decision criteria must be defined as clearly as possible to ensure that the decision criteria in the DP evaluation process are viewed in the same context.

## Slide 27: Investment Strategy for Product Development
Develop Decision Criteria Definitions and Measures
  Development parameters
    Measures and scales developed for the decision criteria must be meaningful in the evaluation process and the data easily accessible.
    Constraints that represent types of DP mixes, qualifiers, and conditions must be identified and differentiated from the evaluation decision criteria.

## Slide 28: Investment Strategy for Product Development
Develop Decision Criteria Definitions and Measures
  The DPs being evaluated represent a broad group of research and development projects.
  It is important that the decision criteria are developed so they could address these varied projects.
  This means that careful consideration must be made so the evaluations of the DPs using the criteria are applicable to the different types of research projects.

## Slide 29: Investment Strategy for Product Development
Goal | Decision Criteria | Description | Measure
Goal 1. Satisfy Customer Needs |  | Customer is defined as the following: • Major Commands (MAJCOMs) • Operating Bases • Test and Evaluation Centers • Intelligence Centers • Aerospace Industry, including primes, subs, suppliers, and vendors | 
 | 1.a Documentable customer need | A user need which is documentable where the need and a point of contact at the customer location can be identified. | Range of 0 to 10 where 0 -- need and Point of Contact not specified 10 -- both are clearly specified
 | 1.b Broad applicability | Broad refers to either broad range of customers, broad range of specific applications (aircraft wings, satellite structure, missile structure), or broad range of systems (F-22, F-117, B-2). | Range of 0 to 10 where 0 -- no direct application 10 -- pervasive
 | 1.c Importance of need to the Military | Importance refers to the priority of the need to the military. | Range of 0 to 10 where 0 -- not demonstrated 5 -- enhances a system 10 -- critical or enabling for system Enhancement is an improvement to performance. The technology allows the military to do what it is doing now, better. Critical is a technology needed to meet system requirements. Enabling is a technology needed to do a new mission.
 | 1.d Breakthrough | Breakthrough technology that could provide a profound impact on a mission capability. | Range of 0 to 10 where 0 -- evolutionary or enhancement 5 -- leaps to state-of-the-art 10 -- provides a unique capability

## Slide 30: Investment Strategy for Product Development
Goal | Decision Criteria | Description | Measure
Goal 2. Make a difference for the Military in this Technical Area. |  |  | 
 | 2.a Leadership | Can we provide the vision for this technical area or set future direction? Are other organizations successfully working in this technical area? Do we have a well-defined niche and the personnel to lead the effort? | Range 0 to 10 where 0 -- no unique role for us 10 -- only we can meet this need
 | 2.b Adequate Funding | Adequacy of the proposed funding. | Range of 0 to 10 where 0 -- unrealistic to do the task 5 -- adequate to meet minimum requirements 10 -- perfect fit of funding to task
 | 2.c Adequate Work Years | Adequacy of the proposed work years, and whether or not the right people are proposed for performing or managing the work. | Range of 0 to 10 where 0 -- unrealistic to do the task 5 -- adequate to meet minimum requirements 10 -- perfect fit of work years/people to task
 | 2.d Payoff | The potential technological payoff of the development effort. | Range of 0 to 10 where 0 -- low 5 -- moderate 10 -- high
 | 2.e Soundness of technical approach | This should include whether or not the approach is scientifically valid, information is presented to support the technical approach, and is logical. | Range of 0 to 10 where 0 -- unreasonable and unsupported 10 -- sound and well thought out

## Slide 31: Investment Strategy for Product Development
Goal | Decision Criteria | Description | Measure
Goal 3. Have a Transition Strategy / Technology Plan |  |  | 
 | 3.a Customer Flow | All customers excluded previously (described in Goal 1) are included. Logical flow of customer to customer planned (logical stages of progression are specified for technology development/ transition /transfer to ultimate customer). Partnerships and/or commitments established. Specific end use requirements identified. | Range 0 to 10 where 0 -- plan is unworkable 10 -- good progression of technology
 | 3.b Risk of Transition Strategy / Technology Plan | Components of risk include: • All key technical issues are addressed • Schedule meets time frame of customer needs • Schedule realistically allows enough time for technology development • Major milestones for each stage of development are defined and measurable • Supporting technology demonstrations (production environment, propulsion, structures, etc.) is in place in time. | Range 0 to 10 where 0 -- risk is unacceptable 10 -- risk is acceptable considering the potential payoff
 | 3.c Leverage of Other Resources | Resources external to normal resources are being used to accomplish development and transition / transfer of this technology. Customer or other government organization is willing to provide some transition funding and/or DP is leveraging core money. | Range of 0 to 10 where 0 -- no attempt to leverage resources 10 -- outstanding use of other resources

## Slide 32: Investment Strategy for Product Development
Establish Group Consensus/Tolerance of Goals and Decision Criteria
  Executives differ in their opinions and objectives for their individual groups.
  It is important to assemble the key decision makers together to discuss in detail, the goals, decision criteria, definitions, measures, and constraints.

## Slide 33: Investment Strategy for Product Development
Establish Group Consensus/Tolerance of Goals and Decision Criteria
  The group agreed on many of the measures.
  Some are refined and redefined to represent the holistic perspective of the group.
  In one or two cases, one Executive Group member agreed to “tolerate” the evaluation criteria to enable the group to gain an overall consensus of how the DPs are measured.

## Slide 34: Investment Strategy for Product Development
Weighting Technical Objectives and Decision Criteria
  A criteria weighting was performed by each of the Executive Group members to develop a group consensus weighting of the high-level goals for the military’s DP evaluation.

## Slide 35: Investment Strategy for Product Development
Weighting Technical Objectives and Decision Criteria
  In the same meeting, the CEO provided sample weightings for the decision criteria established in the meeting and both sets of weights are shown next.
  The weights developed in the Executive Group meeting are only sample weights and are re-established for the actual DP prioritization process.

## Slide 36: Investment Strategy for Product Development
Executive Group Members | Goal 1. Satisfy Customer Needs | Goal 2. Make a Difference for the Military in this Technical Area | Goal 3. Have Transition Strategy /Technology Plan
Member 1 | 78.17% | 14.65% | 7.19%
Member 2 | 76.22% | 6.69% | 17.09%
Member 3 | 70.63% | 9.09% | 20.28%
Member 4 | 72.02% | 15.30% | 12.68%
Member 5 | 60.25% | 24.08% | 15.67%
Member 6 | 16.78% | 54.57% | 28.65%
Member 7 | 10.08% | 74.46% | 15.46%
Consensus | 54.88% | 28.41% | 16.72%

## Slide 37: Investment Strategy for Product Development
Sample Decision Criteria Weighting
  At the same meeting, the CEO weighted the decision criteria associated with each of the goals.
  The resulting weighting factors for the decision criteria have been calculated by multiplying the goals weights by the decision criteria weights.

## Slide 38: Investment Strategy for Product Development
Consensus Weight | Goals | Sample Weights (C.E.O.) | Decision Criteria | Resulting Weight
55% | 1. Satisfy Customer Needs |  |  | 
 |  | 12% | 1.1 Documented | 7%
 |  | 16% | 1.2 Broad Applicability | 9%
 |  | 37% | 1.3 Importance | 20%
 |  | 34% | 1.4 Long Range | 19%
28% | 2. Make a Difference for the Military in this Technical Area |  |  | 
 |  | 55% | 2.1 Leadership | 16%
 |  | 7% | 2.2 Adequate Funding | 2%
 |  | 4% | 2.3 Adequate Work Years | 1%
 |  | 19% | 2.4 Payoff | 5%
 |  | 15% | 2.5 Sound Tech Approach | 4%
17% | 3. Have Transition Strategy /Technology Plan |  |  | 
 |  | 43% | 3.1 Customer Flow | 7%
 |  | 22% | 3.2 Risk of Plan | 4%
 |  | 34% | 3.3 Leverage Other Resources | 6%
 |  |  |  | 100%

## Slide 39: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  The primary stages involved in this task are to evaluate projects with the decision criteria, Prioritize the programs, generate resource allocation decisions and perform sensitivity analysis.
  The facilitators help to lead the military through the process to evaluate DPs with the established decision criteria for the planning period.

## Slide 40: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  The Executive Group are asked to re-weight the goals and decision criteria based on the finalized list of criteria.
  Each of the Executive Group members evaluate the DPs presented to them.
  A group evaluation score is generated from these individual Executive Group DP evaluations.

## Slide 41: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  The budgeting constraints and decision rules to be used in the resource allocation decision process are discussed and finalized.
  Key budgeting targets for research and development for the military overall are established in the areas of space, development cycle, applications areas, and budgeting parameters and set for the overall budgeting process.

## Slide 42: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  The facilitators captured these requirements in an Excel workbook, which is designed to generate instantaneous resource allocation information from the prioritized list of DPs.

## Slide 43: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  A prototype in-house decision support model is developed to provide feedback to the Executive Group on their impact of their votes on the DP prioritization and resource allocation results immediately after the completion of the final DP evaluations by the Executive Group.
  The prioritized list of DPs resulting from this process, with minor modifications, is used by the Executive Group as key input for allocating resources to DPs.

## Slide 44: Investment Strategy for Product Development
Conducting Planning Study and Project Prioritization for Budget Cycle
  All the decision makers had input into the decision process, which ensures objectivity in the DP prioritization process.
  The investment strategy prioritization process provides the foundation for establishing an objective, structured project prioritization and resource allocation process, which provides the military with a traceable and defensible basis for investment decisions.

## Slide 45: Investment Strategy for Product Development

## Slide 46: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Communicate goals and decision criteria and their importance weighting for DP evaluation to managers
    The goals and decision criteria are first re-weighted based on the finalized list of decision criteria.
    A group consensus weighting is generated and then communicated to the managers along with the goals and decision criteria

## Slide 47: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Managers submit/present packages to the Executive Group
    The managers brief the Executive Group with the DPs and provide briefing packets to the Executive Group as required.

## Slide 48: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Executive Group evaluates DPs based on established goals and decision criteria
    Each Executive Group member evaluates, via an evaluation form, the DPs with the established goals and decision criteria.
    Evaluations are combined (averaged) for the group to determine an overall DP evaluation.

## Slide 49: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Generate DP ranking based on DP evaluations and Executive Group weighting of goals and decision criteria
    The goals and decision criteria weighting and project evaluations are the basis for generating the DP ranking.
    The scores from the evaluations are normalized for each project for each individual decision criteria.
    The weighting factors are then applied (multiplied) to the normalized project evaluation scores for each project and these scores are then summed across each decision criteria to generate a score for each DP.
    DPs are then ordered from high to low in rank.

## Slide 50: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Apply budgeting constraints to ranked projects
    Budgeting constraints and budgeting decision rules are applied to the DP ranking to reflect appropriate mixes, qualifiers, and conditions required by the military.
    The result is a constrained project priority and resource allocation scheme.

## Slide 51: Investment Strategy for Product Development
Process Flow Diagram for DP Evaluation Process
  Perform sensitivity analysis
    "What-if" analysis is performed on the ranking and constrained resource allocation to determine the impact of alternate funding schemes on the list of funded DPs.
    This might include revising the weighting scheme, determining "must-have" or "must-fund" projects, and other budgeting decisions that more concisely represent DP funding requirements.

## Slide 52: Investment Strategy for Product Development

## Slide 53: Investment Strategy for Product Development
Develop In-House Tool to Be Used in the Evaluation, Prioritization, and Resource Allocation Process
  A prototype in-house decision support model is developed to meet the military’s requirements for generating real-time prioritization and resource allocation results
    This activity involves developing a software module
    Developing an Excel workbook to capture the prioritization results and generate resource allocation information
    The prioritization module used a multiple criteria decision-making technique TOPSIS

## Slide 54: Investment Strategy for Product Development
Develop In-House Tool to Be Used in the Evaluation, Prioritization, and Resource Allocation Process
  A prototype in-house decision support model is developed to meet the military’s requirements for generating real-time prioritization and resource allocation results
    Most of the budgeting results and reports are keyed off the rank and score generated by the prioritization program.
    Types of “what-if” analysis planned for include
      Changing weighting factors
      Marking projects as funded and unfunded
      Determining the impact on budgets based on budget parameters and constraints

## Slide 55: Investment Strategy for Product Development

## Slide 56: Investment Strategy for Product Development
Example executing of the budget cycle
  This section exemplifies the execution of the budget cycle for the Air Force Material command using the established evaluation framework and the process automated into a decision support tool.

## Slide 57: Investment Strategy for Product Development
Weight the Goals and Decision Criteria
 | Exec Grp 1 |  | Exec Grp 2 |  | Exec Grp 3 |  | Exec Grp 4 |  | Exec Grp 5 |  | Exec Grp 6 |  | Exec Grp 7 |  | Exec Grp 8 |  | Exec Grp 9 |  | Consensus | 
Goals/Decision Criteria | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Weight | Result Weight | Avg Weight | Avg Result Weight
Satisfy Customer Needs | 58.10% |  | 67.50% |  | 28.30% |  | 70.30% |  | 8.30% |  | 58.10% |  | 65.60% |  | 48.00% |  | 69.70% |  | 52.65% | 
Documentable customer need | 33.20% | 19.30% | 34.40% | 23.20% | 7.90% | 2.20% | 5.10% | 3.60% | 8.50% | 0.70% | 37.20% | 21.60% | 21.10% | 13.80% | 31.70% | 15.20% | 56.90% | 39.70% | 26.22% | 13.80%
Broad Applicability | 11.80% | 6.80% | 6.20% | 4.20% | 20.10% | 5.70% | 30.00% | 21.10% | 18.30% | 1.50% | 7.90% | 4.60% | 9.10% | 6.00% | 23.20% | 11.10% | 17.20% | 12.00% | 15.96% | 8.40%
Importance of need to Military | 46.40% | 27.00% | 29.20% | 19.70% | 51.90% | 14.70% | 30.40% | 21.30% | 57.20% | 4.80% | 37.20% | 21.60% | 37.80% | 24.80% | 25.30% | 12.10% | 21.10% | 14.70% | 37.40% | 19.70%
Breakthrough | 8.60% | 5.00% | 30.30% | 20.40% | 20.10% | 5.70% | 34.60% | 24.30% | 16.00% | 1.30% | 17.70% | 10.30% | 32.00% | 21.00% | 19.80% | 9.50% | 4.80% | 3.40% | 20.43% | 10.80%
Make a difference for the Military | 11.00% |  | 26.00% |  | 64.30% |  | 22.30% |  | 72.40% |  | 30.90% |  | 26.50% |  | 11.50% |  | 7.20% |  | 30.22% | 
Leadership | 3.30% | 0.40% | 31.10% | 8.10% | 11.90% | 7.70% | 19.90% | 4.40% | 32.10% | 23.30% | 16.30% | 5.00% | 29.40% | 7.80% | 13.20% | 1.50% | 4.70% | 0.30% | 17.99% | 5.40%
Adequate funding | 37.50% | 4.10% | 9.20% | 2.40% | 5.50% | 3.50% | 7.80% | 1.70% | 9.00% | 6.50% | 5.10% | 1.60% | 7.10% | 1.90% | 17.80% | 2.00% | 25.40% | 1.80% | 13.82% | 4.20%
Adequate work years | 12.80% | 1.40% | 5.50% | 1.40% | 5.50% | 3.50% | 3.10% | 0.70% | 7.70% | 5.50% | 12.70% | 3.90% | 4.60% | 1.20% | 9.00% | 1.00% | 19.50% | 1.40% | 8.91% | 2.70%
Payoff | 18.60% | 2.00% | 35.30% | 9.20% | 30.90% | 19.90% | 53.20% | 11.80% | 13.20% | 9.50% | 32.90% | 10.20% | 20.00% | 5.30% | 22.40% | 2.60% | 14.00% | 1.00% | 26.73% | 8.10%
Soundness of tech approach | 27.80% | 3.00% | 18.90% | 4.90% | 46.20% | 29.70% | 16.10% | 3.60% | 38.00% | 27.50% | 32.90% | 10.20% | 38.90% | 10.30% | 37.60% | 4.30% | 36.50% | 2.60% | 32.55% | 9.80%
Have Trans Strat/Tech Plan | 30.90% |  | 6.50% |  | 7.40% |  | 7.50% |  | 19.30% |  | 11.00% |  | 8.00% |  | 40.60% |  | 23.20% |  | 17.14% | 
Customer Flow | 19.70% | 6.10% | 42.90% | 2.80% | 63.30% | 4.70% | 68.60% | 5.10% | 64.80% | 12.50% | 52.50% | 5.80% | 63.90% | 5.10% | 32.10% | 13.00% | 63.30% | 14.70% | 52.35% | 9.00%
Risk Trans Strat/Tech Plan | 73.80% | 22.80% | 42.90% | 2.80% | 10.60% | 0.80% | 22.00% | 1.60% | 23.00% | 4.40% | 14.20% | 1.60% | 27.40% | 2.20% | 22.50% | 9.10% | 26.10% | 6.00% | 29.15% | 5.00%
Leverage of other resources | 6.50% | 2.00% | 14.30% | 0.90% | 26.10% | 1.90% | 9.40% | 0.70% | 12.20% | 2.40% | 33.40% | 3.70% | 8.70% | 0.70% | 45.40% | 18.40% | 10.60% | 2.50% | 18.50% | 3.20%
 |  |  |  |  |  |  |  |  |  |  |  |  |  | 100.00% |  | 100.00% |  | 100.00% |  | 100.00%

## Slide 58: Investment Strategy for Product Development
Produce Evaluation Forms
Decision Criteria | Measure | Score | Comments
Goal 1. Satisfy Customer Needs |  |  | 
1.a Documentable customer need | Range of 0 to 10 where 0 -- need and Point of Contact not specified 10 -- both are clearly specified |  | 
1.b Broad applicability | Range of 0 to 10 where 0 -- no direct application 10 -- pervasive |  | 
1.c Importance of need to the Military | Range of 0 to 10 where 0 -- not demonstrated 5 -- enhances a system 10 -- critical or enabling for system Enhancement is an improvement to performance. The technology allows the military to do what it is doing now, better. Critical is a technology needed to meet system requirements. Enabling is a technology needed to do a new mission. |  | 
1.d Breakthrough | Range of 0 to 10 where 0 -- evolutionary or enhancement 5 -- leaps to state-of-the-art 10 -- provides a unique capability |  | 
Goal 2. Make a difference for the Military in this Technical Area. |  |  | 
2.a Leadership | Range 0 to 10 where 0 -- no unique role for us 10 -- only we can meet this need |  | 
2.b Adequate Funding | Range of 0 to 10 where 0 -- unrealistic to do the task 5 -- adequate to meet minimum requirements 10 -- perfect fit of funding to task |  | 
2.c Adequate Work Years | Range of 0 to 10 where 0 -- unrealistic to do the task 5 -- adequate to meet minimum requirements 10 -- perfect fit of work years/people to task |  | 
2.d Payoff | Range of 0 to 10 where 0 -- low 5 -- moderate 10 -- high |  | 
2.e Soundness of technical approach | Range of 0 to 10 where 0 -- unreasonable and unsupported 10 -- sound and well thought out |  | 
Goal 3. Have a Transition Strategy / Technology Plan |  |  | 
3.a Customer Flow | Range 0 to 10 where 0 -- plan is unworkable 10 -- good progression of technology |  | 
3.b Risk of Transition Strategy / Technology Plan | Range 0 to 10 where 0 -- risk is unacceptable 10 -- risk is acceptable considering the potential payoff |  | 
3.c Leverage of Other Resources | Range of 0 to 10 where 0 -- no attempt to leverage resources 10 -- outstanding use of other resources |  | 

## Slide 59: Investment Strategy for Product Development
BUDGETING INFORMATION WORK SHEET
Complete one for each new start program
  MAJOR AREA/DIRECTION
  PROJECT NAME
  1. Decision Package Core Program—New Start
  2. YEARLY BUDGET:
    YEAR 1 $
    YEAR 2 $
    YEAR 3 $
    YEAR 4 $ (for core new starts only)
    YEAR 5 $ (for core new starts only)

## Slide 60: Investment Strategy for Product Development
BUDGETING INFORMATION WORK SHEET
Complete one for each new start program
  3. SPACE-RELATED PROJECT? Yes/No
  4. DEVELOPMENT CYCLE:
    Near-term
    Mid-term
    Far-term
  5. APPLICATION:
    Structures
    Propulsion
    Electronics, Optics, Survivabiltiy
    Non-structural

## Slide 61: Investment Strategy for Product Development
Generate Group Evaluation Scores for the DPs
 |  |  |  | Satisfy Customer Needs [52.6%] |  |  |  | Make a Difference for the Military [30.2%] |  |  |  |  | Have A Transition Strategy / Technology Plan [17.2%] |  | 
 |  |  | Weights | 13.8% | 8.4% | 19.7% | 10.8% | 5.4% | 4.2% | 2.7% | 8.1% | 9.8% | 9.0% | 5.0% | 3.2%
Dir | Project Name | Rank | Score | Documnt. customer need | Broad Applic. | Import. of need to Military | Break- through | Leader- ship | Adeq. Fund. | Adeq. Work Years | Payoff | Sound Tech approach | Customer Flow | Risk of Transition Strategy / Technology Plan | Leverage of other resources
6-5 | Mid-term paint roadmap | 1 | 0.8532 | 10.00 | 9.57 | 9.86 | 7.71 | 9.14 | 8.43 | 8.57 | 9.29 | 8.57 | 9.29 | 8.86 | 9.29
6-4 | Gap trtmnt mat for LO airc | 2 | 0.8020 | 10.00 | 8.43 | 9.71 | 8.00 | 8.43 | 8.71 | 8.71 | 9.71 | 8.43 | 8.71 | 8.00 | 6.57
2-3 | Hi cyc fatige of eng blade | 3 | 0.7211 | 10.00 | 9.88 | 10.00 | 6.50 | 8.88 | 6.63 | 6.63 | 9.50 | 8.25 | 7.63 | 7.63 | 7.88
4-1 | Corrosion metrics | 4 | 0.7072 | 8.38 | 9.50 | 9.38 | 8.38 | 7.38 | 8.75 | 8.75 | 9.00 | 8.13 | 8.13 | 7.88 | 6.50
3-4 | Low Energy Curing Resin | 5 | 0.6676 | 8.86 | 8.86 | 8.57 | 8.86 | 9.29 | 7.71 | 8.00 | 9.00 | 7.71 | 8.14 | 7.57 | 8.14
7-1 | VGF growth of InP substrat | 6 | 0.6379 | 8.75 | 9.00 | 8.13 | 8.88 | 8.75 | 8.25 | 8.63 | 8.50 | 9.38 | 8.13 | 8.00 | 7.25
8-1 | Rebaseline core | 7 | 0.6102 | 8.25 | 8.50 | 8.38 | 8.13 | 9.38 | 7.63 | 8.13 | 8.63 | 8.38 | 8.38 | 8.00 | 7.50
6-4 | MS Development II | 8 | 0.5882 | 9.14 | 8.57 | 8.00 | 8.29 | 8.14 | 8.43 | 8.00 | 7.86 | 7.43 | 8.57 | 8.00 | 8.29
8-1 | Electro-optice tunabl filt | 10 | 0.5754 | 8.63 | 8.25 | 8.13 | 9.00 | 8.00 | 7.50 | 7.00 | 8.50 | 7.50 | 7.75 | 7.13 | 7.50
7-4 | Organic Films:enh. EO prop | 9 | 0.5765 | 8.13 | 8.50 | 8.00 | 8.38 | 9.88 | 8.25 | 8.50 | 8.50 | 8.75 | 8.25 | 8.13 | 6.50
4-3 | Probability of Detection | 11 | 0.5664 | 9.50 | 8.13 | 8.75 | 6.00 | 9.38 | 7.25 | 7.31 | 7.25 | 6.88 | 8.63 | 7.88 | 7.75
9-B | St-space proc desg TiAl fo | 12 | 0.5610 | 8.63 | 7.88 | 7.75 | 8.38 | 9.50 | 7.38 | 7.63 | 8.88 | 9.25 | 7.88 | 7.38 | 7.50
3-5 | High Precision Processing | 13 | 0.5596 | 8.43 | 8.86 | 8.29 | 7.43 | 9.00 | 7.71 | 8.14 | 8.29 | 7.14 | 8.43 | 7.14 | 8.57
7-2 | Alternate materl for VLWIR | 14 | 0.5076 | 7.75 | 7.00 | 8.25 | 7.63 | 9.00 | 7.38 | 7.63 | 8.63 | 7.63 | 8.25 | 7.63 | 6.75
4-X | Life manag. of aging systm | 15 | 0.4854 | 8.17 | 9.00 | 8.50 | 5.17 | 8.33 | 7.17 | 7.80 | 8.33 | 7.83 | 8.00 | 8.00 | 7.50
5-X | Invest. strat. for IHPTET | 16 | 0.4850 | 7.38 | 8.25 | 7.88 | 7.75 | 9.13 | 7.50 | 7.57 | 8.50 | 8.38 | 7.75 | 8.00 | 7.50
8-1 | Sacrificial devices | 17 | 0.4748 | 8.31 | 7.38 | 7.38 | 8.13 | 8.13 | 7.50 | 7.38 | 7.75 | 8.38 | 8.38 | 7.13 | 7.13
4-3 | Microwv NDE moist/heat dam | 18 | 0.4586 | 7.75 | 7.50 | 7.75 | 8.63 | 7.13 | 7.38 | 6.75 | 8.14 | 7.25 | 7.63 | 6.38 | 6.25
2-4 | Ti-62222 for the F-22 | 19 | 0.4426 | 9.38 | 7.13 | 7.13 | 5.00 | 8.00 | 8.88 | 8.75 | 7.63 | 8.50 | 9.38 | 8.63 | 7.38
8-1 | Adv. hologrphc. matls/dvcs | 20 | 0.4354 | 7.88 | 7.75 | 7.13 | 7.88 | 8.88 | 7.75 | 7.88 | 7.88 | 8.75 | 7.88 | 7.13 | 7.13
5-3 | Modelng SiP in lrg Ti blts | 21 | 0.4211 | 9.13 | 8.00 | 6.88 | 6.88 | 8.75 | 7.00 | 7.38 | 7.13 | 8.00 | 8.00 | 7.75 | 6.06
2-4 | DRA Scale-up, 6.3(special) | 22 | 0.4052 | 8.88 | 8.13 | 7.25 | 6.00 | 6.38 | 8.38 | 8.25 | 7.88 | 8.50 | 7.38 | 7.88 | 7.00
10-2 | Sealing forc tst methodlgy | 23 | 0.3721 | 8.13 | 8.13 | 7.25 | 6.13 | 8.00 | 8.25 | 8.38 | 7.25 | 8.25 | 7.63 | 7.25 | 7.13
5-1 | Creep resistand oxide fibr | 24 | 0.3586 | 7.50 | 7.63 | 6.88 | 8.38 | 8.25 | 6.25 | 7.00 | 7.29 | 7.00 | 7.00 | 5.63 | 7.00
7-5 | Low temp IR window bonding | 25 | 0.3037 | 7.88 | 6.75 | 7.00 | 6.13 | 7.13 | 7.00 | 7.25 | 7.13 | 7.38 | 8.00 | 7.13 | 6.00
5-2 | Laminatd Struct.Turb.Blade | 26 | 0.3011 | 6.88 | 8.13 | 6.50 | 8.25 | 6.25 | 6.38 | 6.50 | 7.50 | 7.25 | 6.38 | 5.88 | 5.75
7-5 | Multi-spectral Transparenc | 27 | 0.1634 | 6.71 | 7.00 | 6.57 | 6.43 | 7.00 | 6.71 | 6.86 | 7.29 | 7.00 | 6.00 | 6.71 | 4.86
8-2 | Laser processing | 28 | 0.1289 | 6.25 | 7.38 | 6.50 | 5.75 | 7.50 | 6.38 | 6.88 | 7.13 | 7.63 | 5.38 | 6.38 | 6.63

## Slide 62: Investment Strategy for Product Development
Generate Results
Project Name | Calculated Rank | Score
Mid-term paint roadmap | 1 | 0.8532
Gap trtmnt mat for LO airc | 2 | 0.8020
Hi cyc fatige of eng blade | 3 | 0.7211
Corrosion metrics | 4 | 0.7072
Low Energy Curing Resin | 5 | 0.6676
VGF growth of InP substrat | 6 | 0.6379
Rebaseline core | 7 | 0.6102
MS Development II | 8 | 0.5882
Electro-optice tunabl filt | 10 | 0.5754
Organic Films:enh. EO prop | 9 | 0.5765
Probability of Detection | 11 | 0.5664
St-space proc desg TiAl fo | 12 | 0.5610
High Precision Processing | 13 | 0.5596
Alternate materl for VLWIR | 14 | 0.5076
Life manag. of aging systm | 15 | 0.4854
Invest. strat. for IHPTET | 16 | 0.4850
Sacrificial devices | 17 | 0.4748
Microwv NDE moist/heat dam | 18 | 0.4586
Ti-62222 for the F-22 | 19 | 0.4426
Adv. hologrphc. matls/dvcs | 20 | 0.4354
Modelng SiP in lrg Ti blts | 21 | 0.4211
DRA Scale-up, 6.3(special) | 22 | 0.4052
Sealing forc tst methodlgy | 23 | 0.3721
Creep resistand oxide fibr | 24 | 0.3586
Low temp IR window bonding | 25 | 0.3037
Laminatd Struct.Turb.Blade | 26 | 0.3011
Multi-spectral Transparenc | 27 | 0.1634
Laser processing | 28 | 0.1289

## Slide 63: Investment Strategy for Product Development
The budgeting constraints and decision rules are applied to the prioritized list of DPs to generate an initial funding scheme based on available resources.
  Funded DPs—Using DP Budget
  Unfunded DPs – Using DP Budget

## Slide 64: Investment Strategy for Product Development
 | Year 1 - Funded DP Only Calculations |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dir | Project Name | Rank | Score | Funded | Year 1 | Total Allocated Year 1 | Year 2 | Total Allocated Year 2 | Year 3 | Total Allocated Year 3 | Space | Near Term | Mid Term | Far Term | Structures | Propulsion | Electronics, optics, survivability | Non-structural
6-5 | Mid-term paint roadmap | 1 | 0.8532 | Y | 405,000 | 405,000 | 625,000 | 625,000 | 625,000 | 625,000 | - | - | X | - | - | - | - | X
6-4 | Gap trtmnt mat for LO airc | 2 | 0.8020 | Y | 150,000 | 555,000 | 400,000 | 1,025,000 | 600,000 | 1,225,000 | - | - | X | - | - | - | - | X
2-3 | Hi cyc fatige of eng blade | 3 | 0.7211 | Y | 350,000 | 905,000 | 270,000 | 1,295,000 | 213,000 | 1,438,000 | - | - | X | - | - | X | - | -
4-1 | Corrosion metrics | 4 | 0.7072 | Y | 50 | 905,050 | 250 | 1,295,250 | 100 | 1,438,100 | - | - | X | - | X | - | - | -
3-4 | Low Energy Curing Resin | 5 | 0.6676 | Y | 75,000 | 980,050 | 130,000 | 1,425,250 | 100,000 | 1,538,100 | - | X | - | - | X | - | - | -
7-1 | VGF growth of InP substrat | 6 | 0.6379 | Y | 130,000 | 1,110,050 | 200,000 | 1,625,250 | - | 1,538,100 | - | - | X | - | - | - | X | -
8-1 | Rebaseline core | 7 | 0.6102 | Y | - | 1,110,050 | 330,000 | 1,955,250 | 330,000 | 1,868,100 | - | - | X | - | - | - | X | -
6-4 | MS Development II | 8 | 0.5882 | Y | 100,000 | 1,210,050 | 150,000 | 2,105,250 | - | 1,868,100 | - | - | X | - | - | - | - | X
8-1 | Electro-optice tunabl filt | 10 | 0.5754 | Y | 50,000 | 1,260,050 | 150,000 | 2,255,250 | 150,000 | 2,018,100 | X | - | X | - | - | - | X | -
 | Total DP Funding |  |  |  |  | $ 1,260,050 |  | $ 2,255,250 |  | $ 2,018,100 | $ 50,000 | $ 75,000 | $ 1,185,050 | $ - | $ 75,050 | $ 350,000 | $ 180,000 | $ 655,000
 | Total Budget and Goal Allocation |  |  |  |  | $1,288,000 |  | $1,388,000 |  | $2,299,000 | $ 257,600 | $ 322,000 | $ 644,000 | $ 322,000 | $ 450,800 | $ 257,600 | $ 515,200 | $ 64,400
 | % Allocation to Budget |  |  |  |  | 98% |  | 162% |  | 88% | 4% | 6% | 92% | 0% | 6% | 27% | 14% | 51%
 | Goal % |  |  |  |  |  |  |  |  |  | 20% | 25% | 50% | 25% | 35% | 20% | 40% | 5%
 | Over (-) / Under (+) $ |  |  |  |  | $27,950 |  | ($867,250) |  | $280,900 | $ 207,600 | $ 247,000 | $ (541,050) | $ 322,000 | $ 375,750 | $ (92,400) | $ 335,200 | $ (590,600)
 | Over/Under % |  |  |  |  |  |  |  |  |  | 16% | 19% | -42% | 25% | 29% | -7% | 26% | -46%
Funded DPs—Using DP Budget

## Slide 65: Investment Strategy for Product Development
 | Year 1 - Unfunded DPs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Dir | Project Name | Calculated Rank | Score | Funded | Year 1 | Total Un-Allocated Year 1 | Year 2 | Total Un-Allocated Year 2 | Year 3 | Total Un-Allocated Year 3 | Space | Total Un-Allocated Space | Near Term | Total Un-Allocated Near Term | Mid Term | Total Un-Allocated Mid Term | Far Term | Total Un-Allocated Far Term | Structures | Total Un-Allocated Structures | Propulsion | Total Un-Allocated Propulsion | Electronics, optics, survivability | Total Un-Allocated Electronics, optics, survivability | Non-structural | Total Un-Allocated Non-structural
7-4 | Organic Films:enh. EO prop | 9 | 0.5765 | N | 250,000 | 250,000 | 250,000 | 250,000 | - | - | - | - | - | - | 250,000 | 250,000 | - | - | - | - | - | - | 250,000 | 250,000 | - | -
4-3 | Probability of Detection | 11 | 0.5664 | N | 50,000 | 300,000 | 200,000 | 450,000 | 100,000 | 100,000 | - | - | - | - | 50,000 | 300,000 | - | - | 50,000 | 50,000 | - | - | - | 250,000 | - | -
9-B | St-space proc desg TiAl fo | 12 | 0.5610 | N | 265,000 | 565,000 | 360,000 | 810,000 | - | 100,000 | - | - | 265,000 | 265,000 | - | 300,000 | - | - | - | 50,000 | 265,000 | 265,000 | - | 250,000 | - | -
3-5 | High Precision Processing | 13 | 0.5596 | N | 210,000 | 775,000 | 225,000 | 1,035,000 | - | 100,000 | - | - | 210,000 | 475,000 | - | 300,000 | - | - | 210,000 | 260,000 | - | 265,000 | - | 250,000 | - | -
7-2 | Alternate materl for VLWIR | 14 | 0.5076 | N | 350,000 | 1,125,000 | 350,000 | 1,385,000 | 225,000 | 325,000 | 350,000 | 350,000 | - | 475,000 | 350,000 | 650,000 | - | - | - | 260,000 | - | 265,000 | 350,000 | 600,000 | - | -
4-X | Life manag. of aging systm | 15 | 0.4854 | N | 600,000 | 1,725,000 | - | 1,385,000 | - | 325,000 | - | 350,000 | - | 475,000 | 600,000 | 1,250,000 | - | - | 600,000 | 860,000 | - | 265,000 | - | 600,000 | - | -
5-X | Invest. strat. for IHPTET | 16 | 0.4850 | N | 100,000 | 1,825,000 | - | 1,385,000 | - | 325,000 | - | 350,000 | 100,000 | 575,000 | - | 1,250,000 | - | - | - | 860,000 | 100,000 | 365,000 | - | 600,000 | - | -
8-1 | Sacrificial devices | 17 | 0.4748 | N | 50,000 | 1,875,000 | 150,000 | 1,535,000 | 150,000 | 475,000 | - | 350,000 | - | 575,000 | 50,000 | 1,300,000 | - | - | - | 860,000 | - | 365,000 | 50,000 | 650,000 | - | -
4-3 | Microwv NDE moist/heat dam | 18 | 0.4586 | N | 50,000 | 1,925,000 | 250,000 | 1,785,000 | 100,000 | 575,000 | - | 350,000 | - | 575,000 | - | 1,300,000 | 50,000 | 50,000 | 50,000 | 910,000 | - | 365,000 | - | 650,000 | - | -
2-4 | Ti-62222 for the F-22 | 19 | 0.4426 | N | 300,000 | 2,225,000 | 300,000 | 2,085,000 | - | 575,000 | - | 350,000 | 300,000 | 875,000 | - | 1,300,000 | - | 50,000 | 300,000 | 1,210,000 | - | 365,000 | - | 650,000 | - | -
8-1 | Adv. hologrphc. matls/dvcs | 20 | 0.4354 | N | 150,000 | 2,375,000 | 150,000 | 2,235,000 | 150,000 | 725,000 | - | 350,000 | - | 875,000 | - | 1,300,000 | 150,000 | 200,000 | - | 1,210,000 | - | 365,000 | 150,000 | 800,000 | - | -
5-3 | Modelng SiP in lrg Ti blts | 21 | 0.4211 | N | 150,000 | 2,525,000 | 350,000 | 2,585,000 | - | 725,000 | - | 350,000 | 150,000 | 1,025,000 | - | 1,300,000 | - | 200,000 | 150,000 | 1,360,000 | - | 365,000 | - | 800,000 | - | -
2-4 | DRA Scale-up, 6.3(special) | 22 | 0.4052 | N | 150,000 | 2,675,000 | 200,000 | 2,785,000 | - | 725,000 | - | 350,000 | 150,000 | 1,175,000 | - | 1,300,000 | - | 200,000 | 150,000 | 1,510,000 | - | 365,000 | - | 800,000 | - | -
10-2 | Sealing forc tst methodlgy | 23 | 0.3721 | N | 75,000 | 2,750,000 | 75,000 | 2,860,000 | 150,000 | 875,000 | - | 350,000 | - | 1,175,000 | 75,000 | 1,375,000 | - | 200,000 | - | 1,510,000 | - | 365,000 | - | 800,000 | 75,000 | 75,000
5-1 | Creep resistand oxide fibr | 24 | 0.3586 | N | 50,000 | 2,800,000 | 250,000 | 3,110,000 | 200,000 | 1,075,000 | - | 350,000 | - | 1,175,000 | 50,000 | 1,425,000 | - | 200,000 | - | 1,510,000 | 50,000 | 415,000 | - | 800,000 | - | 75,000
7-5 | Low temp IR window bonding | 25 | 0.3037 | N | 200,000 | 3,000,000 | 200,000 | 3,310,000 | 200,000 | 1,275,000 | - | 350,000 | - | 1,175,000 | 200,000 | 1,625,000 | - | 200,000 | - | 1,510,000 | - | 415,000 | 200,000 | 1,000,000 | - | 75,000
5-2 | Laminatd Struct.Turb.Blade | 26 | 0.3011 | N | 100,000 | 3,100,000 | 400,000 | 3,710,000 | 400,000 | 1,675,000 | - | 350,000 | - | 1,175,000 | 100,000 | 1,725,000 | - | 200,000 | - | 1,510,000 | 100,000 | 515,000 | - | 1,000,000 | - | 75,000
7-5 | Multi-spectral Transparenc | 27 | 0.1634 | N | 300,000 | 3,400,000 | 400,000 | 4,110,000 | 400,000 | 2,075,000 | - | 350,000 | - | 1,175,000 | 300,000 | 2,025,000 | - | 200,000 | - | 1,510,000 | - | 515,000 | 300,000 | 1,300,000 | - | 75,000
8-2 | Laser processing | 28 | 0.1289 | N | 50,000 | 3,450,000 | 25,000 | 4,135,000 | - | 2,075,000 | - | 350,000 | 50,000 | 1,225,000 | - | 2,025,000 | - | 200,000 | 50,000 | 1,560,000 | - | 515,000 | - | 1,300,000 | - | 75,000
 | Total Unfunded DPs |  |  |  |  | $ 3,450,000 |  | $ 4,135,000 |  | $ 2,075,000 |  | $ 350,000 |  | $ 1,225,000 |  | $ 2,025,000 |  | $ 200,000 |  | $ 1,560,000 |  | $ 515,000 |  | $ 1,300,000 |  | $ 75,000
Unfunded DPs—Using DP Budget

## Slide 66: Investment Strategy for Product Development
Budget Summary
TOTALS |  |  | 
Budgets | Total | Core New Starts | Remaining DP
Year 1 | $9,811,000 | $8,523,000 | $1,288,000
Year 2 | $17,723,000 | $16,335,000 | $1,388,000
Year 3 | $16,235,000 | $13,936,000 | $2,299,000

## Slide 67: Investment Strategy for Product Development
Budget Summary
YEARLY |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Goal Allocation Percentages | Year 1 Goal Allocation Totals | Year 1 Core New Start Allocation | Year 1 Remaining DP Allocation | Year 1 DP Only Allocation |  | Year 2 Goal Allocation Totals | Year 2 Core New Start Allocation | Year 2 Remaining DP Allocation |  | Year 3 Goal Allocation Totals | Year 3 Core New Start Allocation | Year 3 Remaining DP Allocation
Space | 20% | $1,962,200 | $3,539,000 | ($1,576,800) | $257,600 |  | $3,544,600 | $300,000 | $3,244,600 |  | $3,247,000 | $55,000 | $3,192,000
Total |  | $1,962,200 | $3,539,000 | ($1,576,800) | $257,600 |  | $3,544,600 | $300,000 | $3,244,600 |  | $3,247,000 | $55,000 | $3,192,000
Near Term | 25% | $2,452,750 | $3,415,000 | ($962,250) | $322,000 |  | $4,430,750 | $200,000 | $4,230,750 |  | $4,058,750 | $300,000 | $3,758,750
Mid Term | 50% | $4,905,500 | $3,899,000 | $1,006,500 | $644,000 |  | $8,861,500 | $300,000 | $8,561,500 |  | $8,117,500 | $200,000 | $7,917,500
Far Term | 25% | $2,452,750 | $1,208,000 | $1,244,750 | $322,000 |  | $4,430,750 | $200,000 | $4,230,750 |  | $4,058,750 | $150,000 | $3,908,750
Total | 100% | $9,811,000 | $8,522,000 | $1,289,000 | $1,288,000 |  | $17,723,000 | $700,000 | $17,023,000 |  | $16,235,000 | $650,000 | $15,585,000
Structures | 35% | $3,433,850 | $2,367,000 | $1,066,850 | $450,800 |  | $6,203,050 | $200,000 | $6,003,050 |  | $5,682,250 | $20,000 | $5,662,250
Propulsion | 20% | $1,962,200 | $706,000 | $1,256,200 | $257,600 |  | $3,544,600 | $150,000 | $3,394,600 |  | $3,247,000 | $300,000 | $2,947,000
Electronics,etc. | 40% | $3,924,400 | $4,658,000 | ($733,600) | $515,200 |  | $7,089,200 | $200,000 | $6,889,200 |  | $6,494,000 | $400,000 | $6,094,000
Non-structural | 5% | $490,550 | $791,000 | ($300,450) | $64,400 |  | $886,150 | $30,000 | $856,150 |  | $811,750 | $20,000 | $791,750
Total | 100% | $9,811,000 | $8,522,000 | $1,289,000 | $1,288,000 |  | $17,723,000 | $580,000 | $17,143,000 |  | $16,235,000 | $740,000 | $15,495,000

## Slide 68: Investment Strategy for Product Development
Perform Sensitivity Analysis
  The Executive Group then reviews the constrained DP priority.
  The facilitators are available during the deliberation period for the group to provide real-time updates.
  The Executive Group agrees on the "top half" of the prioritized list of DPs within a short time period
  They accepted the results with minor modifications.

## Slide 69: Investment Strategy for Product Development
Define the Objectives and Identify Metrics
  In this study, significant time and resources are spent to establish a set of goals, objectives, and decision criteria based on the input and views of the executive group.
  The research and development projects that are evaluated with these metrics are broad.
  The executives agreed upon these goals, decision criteria, and metrics for the DP evaluation process and used them for their budget cycle activities.

## Slide 70: Investment Strategy for Product Development
Explore the Environment
  In this study, all the research and development projects that required funding are evaluated.
  All the development labs projects are included in the evaluation.

## Slide 71: Investment Strategy for Product Development
Explore the Scope of the Problem and Its Importance
  In this study, it is important to develop a broad but representative set of decision criteria that could be used to evaluate projects that are varied.
  This requires an evaluation of the holistic environment so that all the functional areas within the command are adequately represented in the evaluation.

## Slide 72: Investment Strategy for Product Development
Explore the Scope of the Problem and Its Importance
  It is also important to not only identify the decision criteria used for the evaluation, but also to ensure that the budget constraints and mix of research represent their strategic objectives.
  This provides a holistic representation of the key considerations that are captured in the budgeting activities.

## Slide 73: Investment Strategy for Product Development
Data Mining and Statistical Analysis
  In this study, it is important to develop a way to capture and represent data from multiple different executives.
  The data that is input into the model and used for the budgeting process needs to be representative of the group consensus for the directorate.

## Slide 74: Investment Strategy for Product Development
Data Mining and Statistical Analysis
  Group decision making techniques are used to capture and aggregate this information from the perspective of decision criteria weighting and DP evaluations
  The data is used to generate the budget cycle results is representative of the group.

## Slide 75: Investment Strategy for Product Development
Solve the Problem and Measure the Results
  This study integrates a number of methods and processes to solve the problem.
  A structured approach to evaluate the DPs is developed and this process is captured in an automated system so that the DPs could be evaluated in real-time.
  The automated model captured the structure of the decision process so that it could be used on an ongoing basis and when resource availability might change.

## Slide 76: Investment Strategy for Product Development
Evaluate the Results and Do Sensitivity Analysis
  The model is structured so that sensitivity analysis could easily be performed.
  In the example budget cycle, the Executive Group performs sensitivity analysis in the process for a short time to generate a budget that meets the group needs.

## Slide 77: Investment Strategy for Product Development
Benefits
  An investment strategy that supports the company’s goals and objectives with decision criteria and metrics related directly to their goals and objectives.
  The framework for a consistent, traceable, and defensible basis for investment decisions.
  A clear quantification of goals, objectives, decision criteria, and measures.

## Slide 78: Investment Strategy for Product Development
Benefits
  A group consensus by key decision makers requiring them to critically examine the company’s objectives and their relative importance.
  All decision makers having a representative say in the final decision-making process.
  A structured approach for the investment strategy becomes the outline for the development of an automated decision support system.
  Confidence in decisions made; an "insurance policy" against inappropriate decisions.

## Slide 79: IMSE 991 Multiple Criteria Decision Making
Lecture 12
Investment Strategy for Product Development in the Aerospace Industry